## Slide 1: CSC358: Principles of Computer Networks
Lecture 1: Introduction
Erfan Meskar
Winter 2025, University of Toronto, Mississauga
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
4G
TCP
Streaming
video

## Slide 2: Today’s Outline
What is the Internet made of?
How does the Internet work?
What is a protocol?
Layering
Sharing

## Slide 3: What is a Network Made of?
Three main components of a network
  End-systems/End-hosts/End-points: send & receive data

## Slide 4: What is a Network Made of?
Three main components of a network
  End-systems/End-hosts/End-points: send & receive data
  Switches & routers: devices that forward data to the destination

## Slide 5: Switches and Routers

## Slide 6: What is a Network Made of?
Three main components of a network
  End-systems: send & receive data
  Switches & routers forward data to the destination
  Links connect end-systems and switches

## Slide 7: Different Types of Links for Different Usages

## Slide 8: Today’s Outline
What is the Internet made of?
How does the Internet work?
  The Internet is similar to the mail delivery system
What is a protocol?
Layering
Sharing

## Slide 9: Mail System
Alice
Bob
U Toronto
McGill U

## Slide 10: Poor Mona Lisa Cannot Fit into an Envelope

## Slide 11: A More Accurate Model
From: Alice, 40 St. George, Toronto
To: Bob, 102 Main St., Montreal, QC
Alice
Bob
From
Address
To
Address

## Slide 12: Multiple Envelope in Pipeline at the Same Time
From: Alice, 40 St. George, Toronto
To: Bob, 102 Main St., Montreal, QC
Alice
Bob
From: Alice, 40 St. George, Toronto
To: Bob, 102 Main St., Montreal, QC
From: Alice, 40 St. George, Toronto
To: Bob, 102 Main St., Montreal, QC
From: Alice, 40 St. George, Toronto
To: Bob, 102 Main St., Montreal, QC
From: Alice, 40 St. George, Toronto
To: Bob, 102 Main St., Montreal, QC

## Slide 13: Mail System
Alice
Bob
U of Toronto
McGill U
Secretary
Secretary

## Slide 14: Characteristics of the Mail System
Each envelope is individually routed
No guarantee of delivery in sequence
No time guarantee for delivery
No guarantee of delivery at all!
  Envelope may be lost

## Slide 15: Internet is Similar to Mail System
Alice
Bob
cs.toronto.edu
www.cs.mcgill.ca
O.S.
O.S.
Header
Data
Header
Data
Packet

## Slide 16: What is a Packet?
A Packet is a chunk of bits which has enough amount of information for it to be independently routed:
  Payload: meaningful only to the endpoints
    Bits from a file, video, etc.
  Header: meaningful to the network and endpoint
    What information must a header contain? The destination address!
Communication between a pair of end-hosts involves the transmission of multiple packets
  “Flow”: stream of packets exchanged between two endpoints (more on this later in the course)

## Slide 17: Packets May Be Damaged
Data
Data
?!%%*

## Slide 18: Packets May Arrive Out of Order
1
2

## Slide 19: Packets May Be Duplicated
Data
Data
Duplicate

## Slide 20: They may not arrive at all!
Data
Data
Full

## Slide 21: Summary So Far
Applications send and receive data in packets …
  … over the Internet which is unreliable.

## Slide 22: Summary So Far
Applications send and receive data in packets …
  … over the Internet which is unreliable.
Packets are forwarded hop-by-hop based on the destination address

## Slide 23: Characteristics of the Internet
Each packet is individually routed
No in-sequence delivery guarantee
No time guarantee for delivery
No guarantee of delivery at all!
No integrity guarantee of data
Packets may be duplicated
Packets can be fragmented (more on this in future)

## Slide 24: Characteristics of the Internet
No in-sequence delivery guarantee
No time guarantee for delivery
No guarantee of delivery at all!
No integrity guarantee of data
Packets can be fragmented
Packets may be duplicated
The Internet cannot be trusted!
It just makes a “best-effort” attempt

## Slide 25: How to be Reliable Over the Unreliable Internet
The end-to-end principle:
  We want to keep the intermediary network devices as simple as possible.
  Complex operations should be implemented at the end-points rather than in the intermediary network devices
So, end-hosts must ensure that all packets are correctly delivered.
  We acknowledge the delivery. But, acknowledging what and how?
  If we do not receive the acknowledgement, we retransmit
    How to determine when to retransmit? Timeout?
    Need local copies of contents of each packet. How long to keep each copy.
    What if an acknowledgement is lost?

## Slide 26: Today’s Outline
What is the Internet made of?
How does the Internet work?
What is a protocol?
Layering and encapsulation
Sharing

## Slide 27: What’s a protocol?
A human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET /path
Host: http://cs.umass.edu

## Slide 28: What’s a protocol?
Network protocols:
  Govern interaction between computers (devices) rather than humans

## Slide 29: What’s a protocol?
All communication activities on the Internet is governed by protocols
Protocols define the rules for:
  … specific messages sent
  … specific actions taken when message received, or other events
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt

## Slide 30: Today’s Outline
What is the Internet made of?
How does the Internet work?
What is a protocol?
Layering and encapsulation
Sharing

## Slide 31: Protocol “layers” and reference models
Networks are complex, with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
  is there any hope of organizing structure of network? and/or our discussion of networks?

## Slide 32: Example: organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
How would you define/discuss the system of airline travel?
end-to-end transfer of person plus baggage

## Slide 33: Example: organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
ticketing service
baggage service
gate service
runway service
routing service
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 34: Why layering?
Layering is an approach to designing/discussing complex systems:
  Explicit structure allows identifying relationship of system’s pieces
  Modularization eases maintenance and updating of system
    change in layer's service implementation: transparent to rest of system applications
    e.g., change in gate procedure doesn’t affect rest of system

## Slide 35: An Introduction to the Internet
Alice
Bob
cs.toronto.edu
www.cs.mcgill.ca
Network Layer
Link Layer
Application Layer
Transport Layer
O.S.
O.S.
Header
Data
Header
Data
Packet

## Slide 36: Layering in the Internet
Link Layer
  Carries data over (usually) point-to-point links between hosts and routers; or between routers and routers.
Network Layer
  Provides “best-effort”, but unreliable, delivery of packets.
Transport Layer
  Provides reliable, in-sequence delivery of data from end-to-end on behalf of application.

## Slide 37: Layered Internet protocol stack
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 38: Services, Layering and Encapsulation
source
transport-layer protocol encapsulates application-layer message, M, with transport-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
application
transport
network
link
physical
destination
application
transport
network
link
physical
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
Application exchanges messages to implement some application service using services of transport layer
M

## Slide 39: Services, Layering and Encapsulation
source
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
network-layer protocol encapsulates transport-layer segment [Ht | M] with network-layer header Hn to create a network-layer datagram/packet
  Hn used by network layer protocol to implement its service
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 40: Services, Layering and Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Link-layer protocol transfers datagram [Hn| [Ht |M] from host to neighboring host, using physical layer services
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services
M
Ht
Hn
Hl

## Slide 41: Encapsulation
message
segment
datagram
frame
Matryoshka dolls (stacking dolls)
Credit: https://dribbble.com/shots/7182188-Babushka-Boi
Notes: Thanks to Nikko Bovornkeeratiroj, Phuthipong <phuthipong@cs.umass.edu>, for the stacking dolls idea and slides

## Slide 42: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
M
message
Ht
M
segment
M
Ht
Hn
datagram
frame
M
Ht
Hn
Hl

## Slide 43
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
source
Ht
Hn
M
segment
Ht
datagram
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical
Encapsulation: an end-end view

## Slide 44: The Classic Picture – OSI Model – The 7-Layer Model
Application – what users see, e.g., web page via HTTP
Presentation – crypto, conversion b/w representations ASCII/Binary
Session – can tie together multiple streams (e.g., audio & video)
Transport – creates a “pipe” to move data between applications
Network – sends packets across entire net., using routing
Data Link – sends frames, handles media access across links
Physical – sends individual bits

## Slide 45: OSI Reference Model
(L7)
(L4)
(L3)
(L2)
Layer N
Protocol: rules for communication within same layer
Layer N-1
Layer N+1
Service: abstraction provided to layer above
API: concrete way of using the service
Layer N uses the services provided by N-1 to implement its protocol and provide its own services

## Slide 46: A More Practical/Realistic Picture
3. Network
2. Link
1. Physical
4. Transport
7. Application
Service: move bits to other nodes across link (Electrical engineering problem)
Service: move frames to other nodes across link (e.g., Ethernet, Wifi, …)
Service: move packets to any other node in the network
IP: Unreliable, best-effort service model
Service: multiplexing applications
Reliable byte stream to the other node (TCP),
Unreliable datagram (UDP)
Service: user-facing application (e.g., HTTP, SSH, …)
Application-defined messages
Where do we handle, e.g., security, reliability, fairness?
Notes: To explain this, I’m going to start in the middle
There are some cross-cutting challenges

## Slide 47: 4-layer Internet Model vs. 7-layer OSI Model
Network
Link
Transport
The 4-layer Internet model
Application
Application
Presentation
Session
Transport
Network
Link
Physical
The 7-layer OSI Model
e.g., IP
e.g., TCP
e.g., Ethernet
e.g., HTTP

## Slide 48: Review: Layering
Separation of concerns
Break problem into separate parts
Solve each one independently
Abstract data from the layer above inside data from the layer below
  “Encapsulation”
Different implementations at one “layer” use same interface
Allows independent evolution
Network
Link
Transport
Application

## Slide 49: Today’s Outline
Mail delivery system and the Internet
What is the Internet made of?
What is a protocol?
Layering and encapsulation
How is a network shared?
  Circuit switching
  Packet switching
  Statistical Multiplexing

## Slide 50: Circuit Switching
It’s the method used used to be used by the telephone network.
A call has three phases:
  Establish circuit from end-to-end (“dialing”),
  Communicate,
  Close circuit (“tear down”).
Originally, a circuit was an end-to-end physical wire.
Nowadays Previously, a circuit was like a virtual private wire:
  each call has its own private, guaranteed data rate from end-to-end.
A
B
Source
Destination

## Slide 51: Circuit Switching
Reservation establishes a “circuit” within a switch
switch
src
dst

## Slide 52
Source
“Caller”
Central
Office
“C.O.”
Destination
“Callee”
Central
Office
“C.O.”
Trunk
Exchange
Each phone call is allocated 64kb/s. So, a 10Gb/s trunk line can carry about 156,000 calls.
Circuit Switching – Telephone Network

## Slide 53: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer
Circuit teardown

## Slide 54: Example of Poor Efficiency in Circuit Switching
The circuit is mostly idle due to traffic bursts
time
Circuit establishment
Data transfer
Circuit teardown

## Slide 55: Example of Poor Efficiency in Circuit Switching
The circuit is used for a short amount of time
Information
time

## Slide 56: Another problem of circuit switching
Circuit switching doesn’t “route around trouble”
A
B

## Slide 57: Circuit Switching, Pros and Cons
Pros:
  Predictable performance
  once circuit is established, it provides simple/fast switching
Cons:
  complexity of circuit setup/teardown
  inefficient when traffic is bursty
  circuit setup adds delay
  switch fails -> its circuit(s) fails

## Slide 58: Packet Switching
It’s the method used by the Internet
Each packet is individually route,
  using the router’s local routing table
The routers maintain no per-flow state
Different packets may take different paths
Several packets may arrive for the same output link at the same time,
  Therefore, a packet switch has buffers

## Slide 59: Packet Switching
A
R1
R2
R4
R3
B
Source
Destination
C
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 60: Packet Switching
A
R1
R2
R4
R3
B
Source
Destination
C
With buffers to absorb transient overloads
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 61
R1
Link 1
Link 2
Link 3
Link 4
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Choose
Egress
“4”
“4”
Packet Switching – Simple Switch Model

## Slide 62
time
rate
One flow
Two flows
Average rate
Many flows
Average rates of: 1, 2, 10, 100, 1000 flows.
Statistical Multiplexing – Basic Idea
Network traffic is bursty, i.e., the rate changes frequently
Peaks from independent flows generally occur at different times
Conclusion: The more flows we have, the smoother the aggregate traffic.
time
time

## Slide 63
Link rate, R
X(t)
Dropped packets
B
Dropped packets
Queue Length
X(t)
Time
Packet buffer
Packets for one output
Data
Hdr
Data
Hdr
Data
Hdr
R
R
R
1
2
N
Packet Switching – Statistical Multiplexing
Because the buffer absorbs temporary bursts,
  the egress link need not operate at rate
But the buffer has finite size, B, so losses will occur

## Slide 64
B
A
time
time
Rate
Rate
C
C
A
C
B
C
Statistical Multiplexing
Notes: Statistical multiplexing
Important if traffic is bursty
Less expensive
Contention requires buffering
Variable delay => no QoS guarantees

## Slide 65
A
B
R
2C
R < 2C
A+B
time
Rate
Statistical multiplexing gain = 2C/R
Other definitions of SMG: The ratio of rates that give rise to a particular queue occupancy, or particular loss probability.
Statistical Multiplexing Gain
Notes: Statistical multiplexing
Important if traffic is bursty
Less expensive
Contention requires buffering
Variable delay => no QoS guarantees

## Slide 66: Why Packet Switching in The Internet
Efficient use of expensive links:
  The links are assumed to be expensive and scarce.
  Packet switching allows many, bursty flows to share the same link efficiently.
  “Circuit switching is rarely used for data networks, ... because of very inefficient use of the links” - Gallager
Resilience to failure of links & routers:
  “For high reliability, ... [the Internet] was to be a datagram subnet, so if some lines and [routers] were destroyed, messages could be … rerouted” - Tanenbaum

## Slide 67: Questions for the rest of the semester
Is layering the best approach?
  Simplifies design
  Yet, limited and inflexible
Best effort service
  Made the rapid growth of the Internet possible
  Makes providing any guarantees very difficult
Packet switching
  Enables statistical multiplexing
  We need extremely fast routers
Routing: How does a router know which output port to send the packet to?